Front bumper removal – Discovery 3

- Remove the upper grille and headlight units as per instructions in the owner manual and remove the towing eye cover

- Remove all visible screws across the front of the bumper assy. Including one in each headlight recess.

- Remove four torx head fasteners underneath the front of the vehicle and one either side holding the bumper to the wheelarch liner

- remove one screw either side located in the headlamp recess as shown below

5.Remove three trim clips (remove the centre expander first, then the trim clip) from inside the wheel arch

6. remove the rearmost trip clip from the wheelarch liner, as shown below

7. Remove two screws from the rear of the wheelarch.

8. Pull away the wheelarch trim from the rearmost edge, at the front there are two toggle clips, which sometimes break off ( I have spares, part number is DYC500010) and the front edge of the trim is located in a slot in the bumper.

With the trim removed, you should see this:-

9. At the top edge of the bumper, there are two Torx fasteners, remove the lower one either side.

10. Push out the two plastic lugs from the locating hole in the wing, pull away the bumper moulding, equally at first, then drivers side so that it swings round to the passenger side, if you have headlamp washers, you’ll need to disconnect the pipe onto the washer bottle, this is a ‘squeeze’ connector – I used a watering can to capture the washer fluid which will run freely

11. Have a cup of tea and a sit down to steady your nerves

12. email me to let me know which bits I forgot….