Pin  Cable Colour   12N Connector Function     12S Connector Function * 

1    Yellow         Left Indicator             Reverse Lamps 
2    Blue           Fog Lamps (if fitted)      Spare 
3    White          Ground                     Ground for pin 4 
4    Green          Right Indicator            Permanent 12V power / charge 
5    Brown          Right Side / Taillamp      Spare 
6    Red            Brake Lamps                Fridge 
7    Black          Left Side / Taillamp       Ground for pin 6 

12N connectors are normally coloured black. Pins 2, 5 and 7 in the plug are female, others are male. 

12S connectors are normally coloured white. Pins 2 and 5 in the plug are female, others are male. 

Note that the 12N and 12S ground wiring must not be connected together and must be connected to the towing vehicle separately via the associated connector. 

* 12S pinouts to post 1999 European standard. Pre-1999 caravans are wired differently