-Remember it is the lower tail gate you need to work on! I am sad to say I spent ages trying to work on the top lift gate

-You will need to be inside the rear of the vehicle. You will need 3 or 4 butter knifes a light and a pair of plies

1. Insert knife blades under tailgate upper trim panel.

2. You will need to pop the carpeted bit out from under the trim

3. You will only have a small gap to work with. You will need to move the foam material aside so you can get you hand in

4. With the palm of your hand facing to the back of the car, insert your hand and locate the lift actuator cable.

5. Follow the cable until you get to the lift actuator.

6. Once you have found the lift actuator, feel for a flexible plastic cover with your fingers... The cover is on the back of the actuator so your fingers need to go under the actuator and push the plastic up with your fingers. This is hard.

7. Find the cable under the plastic. Get the cable into a position where you can get a pair of plies on to it. Pull it to open the door

Once you have done this follow this procedure:

# Tailgate Trim Panel (76.49.23) Tailgate Trim Panel (76.49.23)

## Removal

|  | 11 . | Remove the tailgate upper trim panel. Remove the 4 screw covers. Remove the 4 screws. Release the 2 clips. |
| --- | --- | --- |

|  | 22 . | CAUTIONCAUTION: To protect the paintwork, the tailgate must be supported at all times. Release the 2 support cables from the tailgate. Release the 2 clips. |
| --- | --- | --- |

|  | 33 . | Remove the 2 support cable spigots from the tailgate. |
| --- | --- | --- |

|  | 44 . | Lift the tailgate hinge cover for access. |
| --- | --- | --- |

|  | 55 . | Remove the tailgate trim panel. Release from the 12 clips. |
| --- | --- | --- |

|  | 66 . | NOTENOTE: Do not disassemble further if the component is removed for access only. Remove the 12 clips from the tailgate trim panel. |
| --- | --- | --- |

## InstallationInstallation

|  | 11 . | Install the tailgate trim panel. Install the clips. |
| --- | --- | --- |

|  | 22 . | Lower the tailgate hinge cover. |
| --- | --- | --- |

|  | 33 . | Tighten the support strut spigot to 25 Nm (18 lb.ft). |
| --- | --- | --- |

|  | 44 . | Position the support cables to the tailgate and secure with the clips. |
| --- | --- | --- |

|  | 55 . | Install the tailgate upper trim panel. Secure with the clips. Install the screws. Install the screw covers. |
| --- | --- | --- |

# Liftgate Latch Actuator (86.26.27) Liftgate Latch Actuator (86.26.27)

## RemovalRemoval

|  | 11 . | Remove the tailgate trim panel. For additional information, refer to For additional information, refer to Tailgate Trim Panel (76.49.23) |
| --- | --- | --- |

|  | 22 . | Release the liftgate actuator. Loosen the 2 bolts. Disconnect the electrical connector. |
| --- | --- | --- |

|  | 33 . | Remove the actuator cover. Remove the 2 Torx screws. |
| --- | --- | --- |

|  | 44 . | Remove the liftgate actuator. Release the liftgate latch to actuator cable. |
| --- | --- | --- |

## InstallationInstallation

|  | 11 . | CAUTIONCAUTION: It is possible to incorrectly install the cable, ensure the ferrule and clip are fully engaged. Attach the actuator to the liftgate latch cable. |
| --- | --- | --- |

|  | 22 . | Install the cover. Tighten the Torx screws. |
| --- | --- | --- |

|  | 33 . | Install the liftgate actuator. Tighten the bolts to 10 Nm (7 lb.ft). Connect and secure the electrical connector. |
| --- | --- | --- |

|  | 44 . | Install the tailgate trim panel. For additional information, refer to For additional information, refer to Tailgate Trim Panel (76.49.23) |
| --- | --- | --- |

Being a rough and slow sparkie, I used the inside of a BP connector and a cable tie to fix it. If you are close to a dealer just by the spare part

JD