Parts that I ordered from Digi-Key  USA  1 800 344 4539

http://www.digikey.com/?curr=USD

http://search.digikey.com/us/en/cat/connectors-interconnects/rectangular-housings/1442556?k=mx19

I ordered 2 of the socket housing and 3 of the pin housing, plus 10 each of the mating pins, called socket and pin.  If you do not ever make mistakes, you need only one socket housing and 2 socket housing pins.  For me, it took 3 pins to achieve the goal.  The switch comes with the socket housing already attached.  The cost of my parts was about twenty dollars plus shipping by mail, which was about the same amount.

Pins for the pin housing, connector pin, 20-22 AWG crimp MX19

Digi-Key part number 670-1677-1-ND

Use the above number so you do not have to order 10,000 pins

Connector Pin Housing, 2 position, Grey

JAE part number MX19002P52

The items below, you do not need, as it is already on the switch, but they are nice connectors so I purchased the extra for some future project.

Connector Socket Housing, 2 position, Grey, – what is already on the switch

JAE part number MX19002S52

Pins for the socket housing – connector socket, 20-22 AGW Crimp MX19

Digi-Key part number 670-1678-1-ND

Again, use the above number so you do not have to order 10,000 pins

In summary, you pry out the existing switch, (not that easy), then cut the two conductors as close to the switch as possible, strip the ends, crimp on the two pins, insert them in the rear of the pin housing, plug switch connector into the one you just installed and then tuck the new connector into the recess, (there is a recess to accept the connectors), and then snap the switch back in.  Test for clicking sounds before you do that however.