| Trailer Wiring Color Code |
| --- |
| Connector | Function | Color | Suggested Minimum Wire Gauge | Where To Attach - Vehicle Side | Where To Attach - Trailer Side |
|  |  |  | 4 Way & 5 Way | 6 Way & 7 Way |  |  |
| 7 Way | 6 Way | 5 Way | 4 Way | Right Turn | Green | 18 | 16 | Right turn of vehicle's wiring harness | Trailer's right turn signal |
|  |  |  |  | Left Turn | Yellow | 18 | 16 | Left turn of vehicle's wiring harness | Trailer's left turn signal |
|  |  |  |  | Ground | White | 16 | 12 | Vehicle ground point - metal, uncoated, rustproof | Vehicle ground point - metal, uncoated, rustproof |
|  |  |  |  | Tail / Marker | Brown | 18 | 16 | Taillight of vehicle's wiring harness | Trailer's taillights |
|  |  |  |  | Brake | Blue | 18 | 12 | Electric brake control, power for brakes | Break away switch |
|  |  |  |  | Battery | Red (or Black) |  | 12 | Fuse block or FUSED battery Lead | Break away kit, interior lights and battery charger. |
|  |  |  |  | Back Up | Purple |  | 16 | Back up of vehicle's wiring harness | Back up lights (if available) / Hydraulic coupler. |
| This chart is a typical guide, wire colors may vary based on manufacturers. Use a circuit tester to verify connections. |