Radio Head Display diagnostics procedure

Link to thread

http://www.disco3.co.uk/forum/topic92672.html?highlight=%2Bradio%2Bdisplay&start=15

YouTube video

http://www.youtube.com/watch?v=3hfAfGofb70&feature=youtu.be

I found that I had to hold the right knob in again for another ten seconds or so before the display changed again. You then have to turn the right knob to scroll through the spurious information to find the voltage display and FBH temperature page. 

To access the diagnostics pages on the radio head, the procedure is as follows:

- Ignition must be in position II or better yet, have the engine running and be in Park.

- Turn radio off if it's already switched on.

- Turn radio on by pushing the left knob and, within a few seconds of turning it on.

- Push and hold the right knob in for about 10 seconds (or until the display changes).

- You should then see the Serial Number and some other stuff displayed.

- Push and hold the right knob in again for another ten seconds or so and the display should change again.

- Turn the right knob to scroll through the pages of data, some of it unreadable code.

- Eventually, you will reach the page that shows you the voltage and FBH temperature.

- The 1 VOLT number may show as about 135; the right volt number is the approximate vehicle voltage, 14.1 in my jpg as the engine is running.

- Hold the number 1 keypad button down and the 135 number will slowly decrease.

- I held it until the number reached 118.

- The 118 number seems to be good enough that the radio seems to not do the Low Power Shutdown thing.