Tow Assist – New Trailer

When the vehicle detects the trailer electrics, the Surround Camera system will prompt the driver to confirm if Tow Assist is required.

Selecting [Yes] from the previous screen brings a list of pre-set (or previously saved) trailers. To configure a new trailer select [Add New] and then [OK]

Trailer Setup – Step 1 of 6

Choose from the list of generic trailer descriptive names and select [Next]

Trailer Setup – Step 2 of 6

Position the trailer straight behind the vehicle, to allow more accurate positioning of the target. Stick the self adhesive tracking target to the front of the trailer within the orange highlighted zone as displayed, then select [Next].

The highlighted zone will turn green when the target sticker is correctly positioned.

Trailer Setup – Step 3 of 6

Select the correct number of axles for the chosen trailer, then select [Next]

Trailer Setup – Step 4 of 6

Select the preferred view for use with this trailer, then select [Next]

Hint. The [Side Cameras] view is more suited to tall and/or long trailers such as caravans, whilst the [Reverse Camera] view is more suited to small and/or short trailers.

Trailer Setup – Step 5 of 6

Using the numeric pad, enter the Hitch Length*of the trailer, then select [Next]

*Hitch Length is the distance from the hitch point to the pivot point of the trailer. The pivot point will vary depending on the number of axles, and will be the centre line of the axle on a single axle trailer, the mid point between the axles on a twin axle trailer, the centre line of the centre axle on triple axle trailer etc.

Trailer Setup – Step 6 of 6

Using the distance adjustment buttons, set the orange overlay graphics at the width of the trailer wheels (or trailer edges when a tall trailer is to be used), then select [Finish]

Note. The orange overlay graphics determine the position of the trailer reverse guidance lines.

A confirmation message will appear to show that the trailer has been learnt.

Finally, highlight the trailer that has just been learnt, and select [OK]

NOTE

In order to learn the central position of the trailer, the vehicle must be driven forwards at less than 15mph with the steering wheel in the straight-ahead position. There is currently no confirmation for when this process has completed, however the status can be derived by selecting Reverse gear and noting the presence of message 'Trailer tracking in progress'. Whilst tracking feature is learning the central position, the trailer trajectory lines will appear in a light blue colour, when process is complete they will change to a dark purple colour.

The Tow Assist feature is now ready to use.

Tow Assist – Previously Saved Trailer

When the vehicle detects the trailer electrics, the Surround Camera system will prompt the driver to confirm if Tow Assist is required.

Selecting [Yes] from the previous screen brings a list of pre-set (or previously saved) trailers. Highlight the desired trailer, and select [OK}

NOTE

In order to learn the central position of the trailer, the vehicle must be driven forwards at less than 15mph with the steering wheel in the straight-ahead position. There is currently no confirmation for when this process has completed, however the status can be derived by selecting Reverse gear and noting the presence of message 'Trailer tracking in progress'. Whilst tracking feature is learning the central position, the trailer trajectory lines will appear in a light blue colour, when process is complete they will change to a dark purple colour.

The Tow Assist feature is now ready to use.