Two types of heater air filter, dust only and dust + odor

The air flow is down and that matters re installation of the filter as to direction.

Below is a link to a disco3 pdf written by d3matt that shows the install procedure for replacing the heater air filter.

Air flow is from the top down into the fan.

The post shows using the dark coloured activated carbon filter, the one with the charcoal in between the filter cloth that also removes odor.  The Land Rover part numbers are JKR 500020 or LRO 23977; the Mann part number is CUK 2747

The cheaper “white” filter is the no charcoal filter.  The part number is JKR500010 and is for dust/pollen only. 

The filter with the activated carbon is particularly good removing odor. It does work and if you doubt it, when you find yourself stuck behind a cattle truck, just roll the window down and take a good breath of the "fresh” air.

A jpg in the pdf shows the little flap arrow pointing down and that is correct. It is tricky as the flap is such that one could have the filter oriented correctly and the flap itself down and hence the arrow up. 

I think the purpose of the flap is to provide a tighter friction fit of the filter in the upper rectangular opening. This means that the filter, once loosely inserted, is to be pushed up into the tight rectangular opening so that you do not see the arrow. I did that on mine when I changed it as my dealer said that was the trick, otherwise air bypasses the filter. 

With Land Rover, it seems that there is always a trick to getting it right.

Also I write on the outside edge of mine with felt pen, the date of install. I change it when I change the engine air filter, in my case about once a year, but then we have snow on the ground for six months so dust is not a real concern.

http://www.disco3.co.uk/gallery/albums/use...cement.pdf

http://landroverforums.com/forum/lr3-28/oil-change-notes-pics-2006-lr3-4-0l-v6-52950/